##### WHD型吊式橡胶隔振器

##### WHD suspending rubber vibration absorber

##### Page13

WHD型吊式橡胶隔振器是由金属隔振元件组成，橡胶硬度分成不同等级以满足不同承载能力，具有耐油、耐酸碱、耐高温等性能。该产品阻尼比大，固有频率低，安装方便，对固体传声有明显的降噪效果，主要适用于各种大小设备及管道的吊装隔振。由于橡胶载荷范围大，尤其适用于管道的重量、重心很难精确计算的场合。已使用于国家大剧院风管和设备吊装隔振消声。

WHD suspending rubber vibration absorber is composed of metal outline border and rubber vibration absorbing components．There are different grades of the rubber’s rigidity to meet different loading ability with the capability of resisting to grease，acid，alkali and high temperature．It has large damp ratio and low intrinsic vibration frequency,is convenient to install．It is effective in reducing noises of solid transaudient，is mainly applied for different type of suspending vibration absorbing for large and small equipment and pipelines．It is useful specially when the weight ofpipe and center ofgravity are hard to be calculated because ofthe rubber’S wide load scope．Have been applied to isolating vibration and reducing noise for air conduit and hoisting equipments in National Grand Theater．

#### ZDH、ZHS、VHS型吊式阻尼弹簧隔振器外形尺寸图

#### WHD型吊式橡胶隔振器技术特性表

#### Technological characteristictable

| 规格 type | 承载范围N load scope | 变形范围（mm） distortion scope | 自振频率（HZ） intrinsic vibration frequency | H(mm) | D(mm) | W(mm) | L(mm) | 丝杆直径（mm) diameter of the screw |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| WHD-10 | 50-150 | 5-10 | 10-7 | 100 | 50 | 50 | 46 | M8 |
| WHD-20 | 100-300 | 5-10 | 10-7 | 100 | 50 | 50 | 46 | M8 |
| WHD-30 | 150-450 | 5-10 | 10-7 | 100 | 50 | 50 | 46 | M8 |
| WHD-40 | 200-600 | 5.5-10 | 9.5-7 | 100 | 50 | 50 | 46 | M8 |
| WHD-80 | 400-1200 | 5.5-10 | 9.5-7 | 100 | 50 | 50 | 46 | M12 |
| WHD-160 | 800-2400 | 5-10 | 10-7 | 100 | 60 | 60 | 46 | M12 |
| WHD-320 | 1600-4800 | 5-10 | 10-7 | 120 | 80 | 80 | 56 | M14 |
| WHD-640 | 3200-9600 | 5.5-10 | 9.5-7 | 120 | 80 | 80 | 56 | M16 |
| WHD-1280 | 6400-19200 | 5-10 | 10-7 | 140 | 120 | 120 | 80 | M18 |
| WHD-2560 | 12800-38400 | 5.5-10 | 9.5-7 | 140 | 120 | 120 | 80 | M24 |

#### WHD-D型吊式橡胶隔振器技术特性表

#### Technological characteristictable

| 规格 type | 承载范围N load scope | 变形范围（mm） distortion scope | 自振频率（HZ） intrinsic vibration frequency | H(mm) | D(mm) | W(mm) | L(mm) | 丝杆直径（mm) diameter of the screw |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| WHD-D-10 | 50-150 | 5-10 | 10-7 | 80 | 40 | 70 | 42 | M10 |
| WHD-D-20 | 100-300 | 5-10 | 10-7 | 80 | 40 | 70 | 42 | M10 |
| WHD-D-40 | 200-600 | 5.5-10 | 9.5-7 | 80 | 40 | 70 | 42 | M10 |
| WHD-D-80 | 400-1200 | 5.5-10 | 9.5-7 | 80 | 40 | 70 | 42 | M12 |
| WHD-D-160 | 800-2400 | 5-10 | 10-7 | 105 | 55 | 90 | 56 | M12 |
| WHD-D-320 | 1600-4800 | 5-10 | 10-7 | 105 | 55 | 90 | 56 | M14 |
| WHD-D-640 | 3200-9600 | 5.5-10 | 9.5-7 | 105 | 55 | 90 | 56 | M16 |
| WHD-D-1280 | 6400-19200 | 5-10 | 10-7 | 140 | 70 | 120 | 80 | M18 |
| WHD-D-2560 | 12800-38400 | 5.5-10 | 9.5-7 | 140 | 70 | 120 | 80 | M24 |