##### XD-FLG型浮筑楼板隔振隔声垫

##### XD-FLG-type floating floor building sound isolation pads

##### Page20

浮筑楼板隔振隔声技术是近年来发展较快的一种新型隔振降噪形式，在美国等西方国家广泛应用。它不仅可以隔离内部设备噪声，也可以隔离外界传声，对于具有敏感区域，如下部有重要客房、办公室、会议室、休息室等声学要求很高的场合应当采用该形式。由于隔声设计是个系统工程，包括对围护结构的隔声，机电的隔振和暖通、给排水空调系统的消声和减振等内容。随着国家对环保事业的日益重视，对建筑市场相继出台了《建筑隔声评价标准》（GB/T50121-2005）、《民用建筑隔声设计规范》（GBJ118-88）、《城市区域环境噪声标准》（GB3096-1993）、《城市区域环境振动标准》（GB10070-1988）和《社会生活环境噪声排放标准》（GB22337-2008）等国家标准，目的是规范建筑市场中振动噪声对环境影响的允许范围，从而采取有效措施，达到标准规定的排放要求，使环境更加优美，社会更加和谐。

我公司在十几年的工程实践中，不断总结和开发产品，设计出XD-FLG型浮筑楼板隔振隔声垫、WHG型围护隔声垫，两者配套应用在浮筑楼板上，与金属弹簧隔振器、橡胶隔振器、吊架、支架、托架隔振器、消声器、静压箱、吸身体和隔声门等共同构筑成一个系统的隔振降噪系统，有效地隔离振动和噪声的传递。

XD-FLG型浮筑楼板隔振隔声垫和WHG型围护式隔振隔声垫均采用天然橡胶材料混炼而成，具有空气隔声和阻尼、耐酸碱、耐油、防老化等性能，使用温度为-15~135°C，产品单块面积为500*500和250*250两种，可拼装和裁剪，适用于大面积机电设备的双层隔振隔声。

Floating floor slab vibration of sound insulation technology is rapid development in recent years a new form of vibration and noise, in the United States and other Western countries widely uscd lt can not only isolate the noise within the device can also be isolated outside of the sound,for asensitive area,as the Ministry has an important rooms,offices,conference rooms,lounges and other occasions demanding acoustic should be using this form As the sound design is a systematic projcct,including the building envelope sound insulation,vibration isolation and HVAC mechanicaland electrical,plumbing and air conditioning systems muffler vibration and so on,Along with the growing emphasis on encironmental protection,theconstruction market have issued a "construetion noise evaluation critoria"(GB/T50121-2005),"civil acoustic design specifieation"(GBJ118-88),"Urban Environmental Noise Standard"(GB3096-1993),Urban Area Environmental Vibration Standard "(GB10070-1988)and"social life,environmental noise emission atandards "(GB22337-2008) and other national standards,the purpose is to regulate the construction market in the environmental impact of noiseandvibration allow able range, in order to take effective measures to achieve the emission standards required to make theenvironment more beautiful,more harmonious society,Our company in several year project practices, summarizes and the development product unceasingly,designs XD-FLG to float builds the floor vibration isolation sound insulation pad, the WHG surrounding protection vibration isolation sound insulation pad,both necessary applicationin floats builds on the floor, with the metal spring vibration isolator,the rubber spring vibration isolator,the hanging bracket,the support, the bracket vibration isolator,the silencer,the static pressure,the sound absorption body and the soundproofing gate and so on constructs a system together the vibration isolation noise reduction system,isolates the vibration and the noise transmission effectively.

XD-FLG-floating floor building sound isolation pads and WHG-type envelope-style acoustic isolation pads are made of natural rubber matrrial into the mixing is made with noise and damping the air, acid,oil,anti-aging properties,etc, using the temperatureof-15~135°C,the product of asingle block area 250*500*500 and 250two,can be assembled and cutting,electrical and mechanical equipment for large-scale isolation of double insulation.

##### WHG型围护隔振隔声垫

##### WHG-type sound insulation for exterior vibration pads