##### BW-DJ型单向角向波纹补偿器

##### BW-DJ-type one-way angular bellows compensator

##### Page41

BW-DJ型单向角向波纹补偿器，又称单式铰链型膨胀节，它由波纹管、法兰接管和一对铰链 等结构件组成，只能吸收一个平面内的角位移并能承受波纹管的压力推力。由于吸收一个平面内的角位移，安装时必须与位移平面一致，或采用多个单向角向波纹补 偿器在不同交叉平面内组合安装。当角向变形较大或压力较大时可对产品进行预变形，为增加变形，产品也可有单式制成复式角向波纹补偿器。

W-DJ-type one-way angular bellows compensator, also called Single hinge-type expansion joint, is made up of bellows, flange connecting pipe and a pair of hinge etc.It can only absorb angular displacement in one plane and bear the pressure of the bellows. So it should be consistent with the plane of displacement when ins-talled, or it can also be assembled by several single-direction angular compensators in different crossed planes. If the angular displacement or the pressure is large, a pre-deformation is requi-red. To increase deformation, the product can also be changed from single angular corrugated compensator to duplex one.

#### 技术特性表： 疲劳寿命1500次
technical characteristics table: weary life of 1500 times.

| 公称通径 mm nominal diameter | 长度 mm length | 波级管有效面积 cm2 effective area of bellows | 角向补偿量（土）/刚度N/mm angular compensating quantum士mm mm/rigidity N/mm |
| --- | --- | --- | --- |
|  |  |  | 1.0mpa | 1.6mpa | 2.5mpa |
| 40 | 300 | 21 | 4 | 6 | 4 | 13 | 4 | 16 |
| 50 | 300 | 41 | 4 | 7 | 4 | 15 | 4 | 18 |
| 65 | 350 | 61 | 6 | 8 | 6 | 10 | 6 | 12 |
| 80 | 350 | 82 | 6 | 14 | 8 | 18 | 8 | 25 |
| 100 | 350 | 125 | 8 | 15 | 8 | 25 | 8 | 50 |
| 125 | 400 | 180 | 10 | 28 | 10 | 40 | 10 | 55 |
| 150 | 400 | 255 | 10 | 30 | 10 | 85 | 10 | 105 |
| 200 | 450 | 480 | 12 | 55 | 12 | 145 | 8 | 220 |
| 250 | 450 | 730 | 12 | 130 | 12 | 200 | 10 | 360 |
| 300 | 500 | 1020 | 12 | 180 | 12 | 270 | 10 | 420 |
| 350 | 550 | 1280 | 14 | 200 | 12 | 420 | 10 | 450 |
| 400 | 550 | 1580 | 14 | 260 | 12 | 440 | 10 | 1350 |
| 450 | 600 | 1980 | 12 | 350 | 12 | 750 | 10 | 1400 |
| 500 | 650 | 2450 | 12 | 510 | 12 | 930 | 10 | 1500 |
| 600 | 700 | 3450 | 10 | 1100 | 10 | 1600 | 8 | 2800 |
| 700 | 750 | 4740 | 8 | 1500 | 6 | 1900 | 6 | 3200 |
| 800 | 750 | 5960 | 6 | 1600 | 5 | 2300 | 4 | 3800 |
| 900 | 800 | 7560 | 4 | 2000 | 3 | 2800 | 3 | 4600 |
| 1000 | 850 | 9280 | 4 | 5000 | 3 | 8000 | 2 | 10000 |
| 1100 | 900 | 10816 | 3 | 11000 | 2 | 12800 | 2 | 15000 |
| 1200 | 900 | 13010 | 2 | 15000 | 2 | 16000 | 2 | 18000 |
| 1300 | 1000 | 14800 | 2 | 16000 | 2 | 18500 | 2 | 21000 |
| 1400 | 1000 | 16510 | 2 | 19800 | 2 | 24000 | 2 | 28000 |
| 1500 | 1100 | 18900 | 2 | 21000 | 2 | 28000 | 2 | 31000 |
| 1600 | 1200 | 21920 | 2 | 26000 | 2 | 31000 | 2 | 36500 |