##### XWQ型隔振台座限位器

##### XWQ vibration isolation dado restrictor

##### Page11

XWQ型隔振台座限位器由带铰链机构的钢板与橡胶组成，主要针对高层建筑内水泵开启与关闭时台面振幅较大，容易引起管路错位暴裂而设计的，具有性能稳定，价格便宜等优点，现已广泛使用于需要限位的动力设备中。

XWQ vibration isolation dado restrictor is com－posed of steel plant with hinge and rubber．It is designed for large swing of table board when the water pump is on or off in the high buildings，which will result in the pit)eline disloc-ation．It has stable per for mance and cheap price．It has been widely used in power equipments to which the restrictor is needed．

XWQ型技术特性表
　Technological characteristic table

| 规格 Specification | 承载范围（kg） load scope | A | B | C | D | E | F | G | T |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| XWQ-500 XWQ-1000 | 0-500 500-1000 | 80 | 200 | 40 | 2 | 80 | 80 | 65 | 8 |
| XWQ-2000 XWQ-4500 | 1000-2000 2000-4500 | 120 | 320 | 65 | 4 | 130 | 130 | 120 | 14 |
| XWQ-9800 XWQ-20000 | 4500-9800 9800-20000 | 180 | 400 | 110 | 5 | 220 | 220 | 200 | 26 |

FS型环形橡胶隔振器由上下钢板，中间环状橡胶块组成，分二层、三层，自振频率低，性能稳定，适用于水泵、风机、压缩机等动力设备隔振。

FS ringy rubber vibration absorber is composed oftop and bottom steel plate and ringy rubber block in the middle．It has two—layer and three-layer series，has low intrinsic vibr-ation frequency and stable perfor-mance，is effective in vibration absorbing for power equipment，such as water pump，fan engine and compressor．

FXG型技术特性表
Technological characteristic table

| 规格 Specification | 承载范围（kg） load scope | 最大变形（mm） distortion scope | 自振频率（HZ） intrinsic vibration frequency | D | H | A | B | d1 | d2 | t |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FS-2-60 FS-3-60 | 30-80 30-80 | 9 13 | 7 6 | 60 60 | 35 51 | 105 105 | 83 83 | M8 M8 | 11 11 | 2.5 2.5 |
| FS-2-80 FS-3-80 | 60-150 60-150 | 11 15 | 6.3 5.1 | 80 80 | 47 65 | 140 140 | 110 110 | M10 M10 | 13 13 | 3 3 |
| FS-2-120 FS-3-120 | 120-300 120-300 | 18 27 | 5 4 | 120 120 | 67 98 | 210 210 | 165 165 | M12 M12 | 15 15 | 3 3 |
| FS-2-160 FS-3-160 | 280-700 280-700 | 25 39 | 4.4 3.5 | 160 160 | 86 126 | 280 280 | 220 220 | M16 M16 | 19 19 | 4.5 4.5 |

TL型推力限位器是由一弹簧组件与橡胶隔振消声垫串联组成，它可在厂内预校准其推力以及在工地上作进一步调校，令其在开始工作和停止工作之间有一定的移动距离，一般控制在最大8mm的位移量，可在水平和垂直方向作限位使用。

TL thrust restrictor is composes of a set of spring assembly and rubber vibr-ation and noise isolation mat．Thrust of the product can be preliminary adjusted in the factory and further adjusted on build-ing site．It should keep a certain moving distance between starting and ending work． Under normal condition，the maximum moving distance should be less than 8mm by horizontal and vertical restricted using．

T L型技术特性表
Technological characteristic table

| 规格 Specification | 最大推力N maximum thrust | 变形（mm） Distortion | 刚度N/mm Rigidity | H | W1 | W2 | L1 | L2 | L3 | M | d |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TL-30 | 300 | 25 | 12 | 130 | 110 | 70 | 130 | 30 | 70 | M12 | ø13 |
| TL-70 | 700 | 25 | 27 | 130 | 110 | 70 | 130 | 30 | 70 | M12 | ø13 |
| TL-150 | 1500 | 25 | 59 | 130 | 110 | 70 | 130 | 30 | 70 | M12 | ø13 |
| TL-300 | 3000 | 25 | 118 | 130 | 110 | 70 | 130 | 30 | 70 | M16 | ø13 |
| TL-500 | 5000 | 25 | 196 | 130 | 110 | 70 | 130 | 30 | 70 | M16 | ø13 |
| TL-750 | 7500 | 25 | 294 | 130 | 110 | 70 | 130 | 30 | 70 | M18 | ø13 |
| TL-1000 | 10000 | 25 | 392 | 130 | 110 | 70 | 130 | 30 | 70 | M18 | ø16 |
| TL-1300 | 13000 | 25 | 540 | 130 | 110 | 70 | 130 | 30 | 70 | M20 | ø16 |
| TL-1800 | 18000 | 25 | 720 | 130 | 110 | 70 | 130 | 30 | 70 | M20 | ø16 |