##### TL型推力限位器

##### TL thrust restrictor

##### Page11

TL型推力限位器是由一弹簧组件与橡胶隔振消声垫串联组成，它可在厂内预校准其推力以及在工地上作进一步调校，令其在开始工作和停止工作之间有一定的移动距离，一般控制在最大8mm的位移量，可在水平和垂直方向作限位使用。

TL thrust restrictor is composes of a set of spring assembly and rubber vibr-ation and noise isolation mat．Thrust of the product can be preliminary adjusted in the factory and further adjusted on build-ing site．It should keep a certain moving distance between starting and ending work． Under normal condition，the maximum moving distance should be less than 8mm by horizontal and vertical restricted using．

#### TL型技术特性表

#### Technological characteristic table

| 规格 Specification | 最大推力N maximum thrust | 变形（mm） Distortion | 刚度N/mm Rigidity | H | W1 | W2 | L1 | L2 | L3 | M | d |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TL-30 | 300 | 25 | 12 | 130 | 110 | 70 | 130 | 30 | 70 | M12 | ø13 |
| TL-70 | 700 | 25 | 27 | 130 | 110 | 70 | 130 | 30 | 70 | M12 | ø13 |
| TL-150 | 1500 | 25 | 59 | 130 | 110 | 70 | 130 | 30 | 70 | M12 | ø13 |
| TL-300 | 3000 | 25 | 118 | 130 | 110 | 70 | 130 | 30 | 70 | M16 | ø13 |
| TL-500 | 5000 | 25 | 196 | 130 | 110 | 70 | 130 | 30 | 70 | M16 | ø13 |
| TL-750 | 7500 | 25 | 294 | 130 | 110 | 70 | 130 | 30 | 70 | M18 | ø13 |
| TL-1000 | 10000 | 25 | 392 | 130 | 110 | 70 | 130 | 30 | 70 | M18 | ø16 |
| TL-1300 | 13000 | 25 | 540 | 130 | 110 | 70 | 130 | 30 | 70 | M20 | ø16 |
| TL-1800 | 18000 | 25 | 720 | 130 | 110 | 70 | 130 | 30 | 70 | M20 | ø16 |